## Slide 1: ET TUTORIAL
Magnetic Circuits

## Slide 2
Ans: 3.16 A
1. A circular ring has a mean circumference of 1.5m and a cross-section area of 0.01 m2. A saw cut of 4mm wide is made in the ring. Calculate the magnetizing current required to produce flux of 0.8mWb in the air gap if the ring is wound with a coil of 175 turns. ( Assume leakage factor = 1.25)

## Slide 3
Ans: 2387 AT
2. A cast steel electromagnet has an air gap length of 3mm and an iron path of length 40 cm. Find the number of ampere-turns necessary to produce a flux density of 0.7 Wb/m2 in the air-gap. Neglect leakage and fringing. Assume ampere-turns required for air gap to be 70% of the total ampere-turns.

## Slide 4
Ans:
3. In the magnetic circuit shown in Fig. below the area of cross-section of the central limb is 12 cm2 and that of each outer limb (A to B) is 6 cm2. A coil current 0.5 A produces 0.5 mWb in the air-gap. Find the relative permeability of the core material.

## Slide 5
Ans:

## Slide 6
Ans:
b) A
5. For the magnetic circuit of Fig. below.
(a) Calculate the energy stored in the core and in the air-gap for a coil current of 4 A.
(b) Calculate the excitation current and induced emf in the coil to produce a flux of mWb in the air-gap.

## Slide 7
Ans: 3.51A
6. An iron ring of cross-section area 6cm2 is wound with a wire of 100 turns and has a saw cut of 2 mm. Calculate the magnetizing current required to produce a flux of 0.1mWb if the mean length of the magnetic path is 30cm and the relative permeability of iron is 470.