## Slide 1: 1. A 400V, 3phase 4 wire system of the figure has a star connected load with ZA = 10ohm, ZB= 15+j10 ohm and ZC = j5 ohm. Find the line currents and current through the neutral conductor.
Phase currents:
IA = 23.094 A, 0o
IB = 12.81A , -153.69o
IC= 46.19A , 30o
IN= 54.47A, 18.65o

## Slide 2: 2. A 100V, 3phase 3 wire supply feed an unbalanced star connected load with an impedance of ZR =5ohm, ZY = j2 ohm and ZB= -j4 ohm, find the phase and line currents using star delta transformation.
Phase currents:
IRY = 31.25, -38.66o A
IYB= 39.06, -68.66o A
IBR= 15.63,-98.66o A
Line currents:
IR= 27.06, -8.65o A
IY= 19.7, -121.14o A
IB= 26.69, 128.36o A

## Slide 3: 2. A three phase supply with a line voltage of 250V has an unbalanced delta load as shown in the figure. Determine the phase and line currents, total active and reactive power if the phase sequence is ABC
Phase currents:
IAB= 12.5 A, 0o, IBC= 16.66 A, -140o
ICA= 10 A, -330o
Line currents:
IA = 6.3 A, -52.48o, IB= 27.45 A, -157.02O,
IC= 26.57A, 36.25o
Active power:
PAB = 3.13kW, PBC= 3.92kW, PCA= 0W,
Pt= 7.05kW
Reactive power:
QAB= 0kVAR, QBC= 1.43kVAR, QCA= 2.5kVAR
Qt= 3.93kVAR

## Slide 4: 5. In the circuit, a 400 V, 50 Hz, 3-phase supply of phase sequence ABC is supplied to a delta-connected load consisting of a 100 W resistor between lines A and B, a 378 mH inductor between lines B and C, and a 37.8 μF capacitor between lines C and A. Determine phase and line currents.
Phase currents
line currents

## Slide 5: 5. Calculate the phase currents of b and c and find out which bulb glows brighter.
Ic =0.259, 123.06deg
Ib = 0.91 , 225.36 deg
Bulb ABC glows brighter

## Slide 6: 6. Find the line currents and the power absorbed by the delta-connected load